## Slide 1: HW #1: 32-bit ALU Design
Chun-Jen Tsai
NYCU
02/29/2024

## Slide 2: HW 1: Design a 32-bit ALU
Goal: design an ALU module using Verilog.
  An Arithmetic and Logic Unit (ALU) is the circuit module of a CPU that performs calculations on registers
  This ALU will become part of a mini processor for future HW
  Verilator and GTKWave will be used as logic simulation tools
The deadline of the HW is on 3/14, by 5:00pm.

## Slide 3: The Port Definition of the ALU
The ALU module is a combinational circuit with the I/O ports defined as follows:
  op triggers one of the six operations shown in the next slide
  All output signals shall be set to 0 if op is an invalid bit pattern
module alu #(parameter DWIDTH = 32)
(
input [3 : 0] op, // Operation to perform. input [DWIDTH-1 : 0] rs1, // Input data #1. input [DWIDTH-1 : 0] rs2, // Input data #2.
output [DWIDTH-1 : 0] rd, // Result of computation. output zero, // zero = 1 if rd is 0, 0 otherwise.
output overflow // overflow = 1 if overflow happens.
);

## Slide 4: Operation Table of the ALU
You must implement 6 operations in the ALU
  Any input bit patterns to the port op not listed in the table will be considered invalid.
ALU operation | Function | op
and | rd  rs1 and rs2 | 0000
or | rd  rs1 or rs2 | 0001
add | Signed addition: rd  rs1 + rs2 | 0010
sub | Singed subtraction: rd  rs1 - rs2 | 0110
nor | rd  ~(rs1 or rs2) | 1100
slt | rd  (rs1 < rs2)? 32’h1 : 32’h0; | 0111

## Slide 5: Coding Comments
You don’t have to implement the 32-bit adder and subtractor at gate-level. You can simply use the Verilog operators + and – to do the job
For the implementation of the overflow flag, please refer to section 3.2 of the textbook
  Note that integers are represented in 2’s complement here
  Overflow conditions for additions and subtractions:

## Slide 6: Guide to the Simulation Tools
For this course, we will use Verilator as the waveform simulator and GTKWave as the waveform viewer for digital circuit designs
A user’s guide on how to install and get started with the tools under Linux or Windows Subsystem for Linux (WSL) is available in the following link: https://hackmd.io/SQHK4lmSR1-Ob9V9Osrz5A
  Note that the Verilator installed using the command: $ sudo apt install verilator under ubuntu may be too old, so you have to build your own Verilator from the source

## Slide 7: HW 1 Grading Guide
You should upload your alu.v to E3 by the deadline
The port declaration of your ALU module must follow the specification in this HW precisely
A sample testbench, HW1_tb.tgz, is available on E3
  Please read the readme.txt file in the package carefully
For grading, TAs will use a more thorough testbench to test your design
  Correctness of rd account for 70%
  Correctness of zero and overflow account for 30%